## Slide 1
Report on the separation protocol set in CONSORCIO

## Slide 3: Separation protocol for bulky waste in Valencia area
What separation protocol for bulky waste not suitable for reuse
To provide materials for high added value recycled products
Notes: This action is about defining what separation protocol should follow the bulky waste not suitable for reuse in the local conditions of the collection facilities of CONSORCIO (Valencia area) to provide the most efficient way materials to be used as a basis for research to obtain high added value recycled products

## Slide 4: Methodology
Bulky waste accumulated according to the proposed classification, to test the quantities collected from each flow in 3 weeks.
Review of the proposed segregation
Re-organisation of separation system suitable for CAS and suitable for sorting facilities.
Notes: Bulky waste from the Civic Amenity Sites (CAS) closest to Caudete de las Fuentes plant was accumulated in this plant according to the proposed classification, in order to test the quantities collected from each flow.
Once obtained the information of quantities collected according to the proposed segregation, the distribution of containers is reconsidered and decisions are made as to what separation makes sense in the CAS and what separation makes sense in sorting facilities.

## Slide 5: Results
In case of container availability:
Possible to pick up foam mattresses and springs separately, avoiding manipulating the waste in the sorting facility.
Possible to collect in a separate container hard plastic.
Too few bulky textiles for separate collection.
Notes: After accumulating the corresponding bulky waste streams during the three weeks of testing in October and November 2016, and separating in the sorting facility of Caudete de las Fuentes materials not separated in origin (bulky textiles, hard plastics and various types of mattresses), the following results are obtained:
The quantity of mattresses collected would allow, in the case of container availability, to pick up foam mattresses and springs separately, avoiding manipulating the waste in the sorting facility.
Likewise, it would be possible to collect in a separate container hard plastic, in case there is room for an additional container.
On the contrary, the amount of bulky textiles is so small that it does not justify the separate collection of this flow.

## Slide 6: Conclusions (1)
Based on the test, here is the new separation protocol by containers to get materials covered by URBANREC actions:
Garden debris (biodegradable waste - garden and park waste)
Construction and demolition waste (mixed construction and demolition waste)
Non-hazardous bulky WEEE
Ferrous scrap (metals, discarded electrical and electronic equipment other than in previous point)

## Slide 7: Conclusion (2)
Bulky wooden items (furniture, boards, etc.)
Furniture made of various materials. (Wood, metal, textiles, foams…)
Mattresses (PU Foam mattresses, latex mattresses, spring mattresses...)
  Foam mattresses
  Spring mattresses
Mixed bulky waste (Any bulky waste not included in the precedent categories)
Bulky hard plastics